Electronics II / Problem sheet 3 / P. Stallinga	MIEET 3º ano

1:
The figure above shows a differential pair based on FETs with a current source of 2 mA that has an output resistance of 200 kΩ. The FET-parameters are: K = μCoxW/L = 2 mA/V2 and VT = 0. RD = 5 kΩ.
a) Calculate the bias point of the circuit.
b) Calculate the common-mode gain, Acm, the differential-mode gain Adm, and the CMRR.
c) Calculate the inpute resistance rin and output resistance rout of the circuit.
FET:
ID = K (VGS-VT)VDS (linear)
ID = K/2 (VGS-VT)2 (saturation)

2:
In the theoretical lectures we found a relation between the input signal difference (V1 e V2) and the output currents (IE1 e IE2) for large signals (Ebers-Moll) for a differential pair based on bipolar transistors. The conclusion there was that the output signal is linear proportional to the input signal difference until about 3 times VT, in other words about 75 mV.
Repeat the calculations for a differential based on FETs.
(Difficult! You can use electronics simulators such as SPICE or Workbench)