Electronics II / Problem sheet 4 / P. Stallinga	MIEET 3º ano

The figure above shows an equivalent circuit of an common-source FET amplifier. The input signal comes from a signal generator with an output resistance R. Rin represents the input resistance of the FET stage and is caused by the gate-bias resistances. RL' is the parallel equivalent resistance composed of load RL, drain resistance RD and FET output resistance ro. Capacitors Cgs and Cgd are internal capacitors of the FET.
R = 100 kΩ, Rin = 420 kΩ, Cgs = Cgd = 1 pF, gm = 4 mA/V, RL' = 3.33 kΩ.

a) Determine the mid-band gain, Av = vo/vi.
b) Determine the bandwidth of the circuit.