Electronics II / Problem sheet 5 / P. Stallinga	MIEET 3º ano

For the (positive) feedback system of Figure 1, determine the relation between Vi and Vo. / color red {A_f} = color red {A over (1 - A %beta)}

Fill out the table below with gain values Af ≡ Vo/Vi for combinations A-β.

β \ A	∞	105	104	1000	100	10	1
−1	1	1	1	1	0.99	0.91	0.05
−0.1	10	10	9.99	9.9	9.09	5	0.91
−0.01	100	99.9	99.01	90.91	50	9.09	0.99
−10−3	103	990.1	909.09	500	90.91	9.9	1
−10−4	104	9090.91	5000	909.09	99.01	9.99	1
0	∞	105	104	1000	100	10	1
+0.1	−10	−10	−10.01	−10.1	−11.11	∞	1.11
+1	−1	−1	−1	−1	−1.01	−1.11	∞

For an open-loop gain, A = 105 with a variation (tolerance) of 5%. Calculate the variation of closed-loop gain for the following betas:

β = 0	β = −0.001	β = −0.01	β = −0.1	β = −1
5%	0.0495%	0.005%	0.0005%	0.00005%

The amplifier A (A = 105) has a single pole at 10 Hz. Determine the bandwidth of the circuit with feedback of β = −10−3.

The gain-bandwidth product is constant. Without feedback Av x Δf = 105 x 10 Hz = 1 MHz. With feedback of β = −10−3, the gain becomes (see the table above) 990.1. The bandwidth therefore is Δf = 1 MHz/ 990.1 = 1.01 kHz. Another way of calculating is: Δf = Δf0 (1 − Aβ) = 10 Hz x (1 + 105 x 103) = 1010 Hz.