Electronics II / 2009-2010 mod. 1 / Problem sheet 6 / P. Stallinga	MIEET 3º ano

Figure 1: System with negative feedback. A is the open-loop gain (without feedback), β is the feedback factor.

a) Determine the relation between input signal and output signal, Af ≡ Vo/Vi.

The ideal amplifier (rin = ∞, e rout = 0) has an open-loop gain of 105 and has poles at 10 Hz, 1 kHz, 100 kHz and 1 MHz.

The feedback is made of resistances (passive elements that do not change the phase) and is given as β = 0.5.

b) Determine the DC gain.

Determine if the amplifier with feedback is stable (Phase margin: 45º). For this

c) Make Bode plots and Nyquist plots and draw conclusions. For what range of frequencies does the system run the risk of oscillating?

d) For what value of β the system is marginally stable?

e) Repeat paragraphs a) .. d) for the same system, but with positive feedback (see figure below).

Figure 2: System with positive feedback.